## Slide 1: ENGI 301 Smart Vanity Mirror Proposal
November 9, 2021
Nneoma Ome

## Slide 2: Background Information
The goal of this project is to develop a smart vanity/desk mirror that allows a user to view their appearance and displays information that may be relevant for daily use (i.e., calendar date, time, temperature, weather forecast etc.
Although there are existing projects centered around developing smart mirrors, many of the projects have large monitors, mirrors, and frames that make it difficult for the vanity to be portable. Additionally, the mirrors made in the existing projects are not intended to be vanity mirrors, so they tend to lack a lighting component and those that do include lighting strips use them for backlighting and not for enabling the user to have better visibility of their image.
As such, my project will include the following features to match and improve upon the features in existing projects:
  Clean, aesthetic finish
  Easel stand
  Portable size
  LED lighting projected towards user with button to turn on/off
  Touchscreen functionality and modules for users to interact with
    Backup toggle/Navigation button in case touchscreen functionality does not cooperate
  Internet connection: video player, music, weather
The features listed above will make the device particularly useful to students and people that move frequently as its portable size allows for it to be used on many surfaces as opposed to being mounted on a wall or to a table.
Links to Existing Projects:
  https://www.hackster.io/mprocter12/smart-mirror-using-beaglebone-black-e379a3
  https://www.hackster.io/eben-kouao/smart-mirror-touchscreen-with-face-recognition-6c84cc
Links to Existing Libraries:
  https://github.com/MichMich/MagicMirror
Wrought Studio Lighted Makeup Mirror Hollywood Mirror Vanity Makeup Mirror With Lights Smart Touch Control 3-Gear Dimable Light 360°Rotation
Image of Existing Project on Hackster
Image of Existing Project on Hackster
Allure Smart Makeup Mirror
Notes: Image 1 Source: https://www.wayfair.com/Wrought-Studio™--Lighted-Makeup-Mirror-Hollywood-Mirror-Vanity-Makeup-Mirror-With-Lights-Smart-Touch-Control-3Gear-Dimable-Light-360°Rotation-X117120506-L41-K~W006019495.html?refid=GX549028497019-W006019495&device=c&ptid=1433750947875&network=g&targetid=pla-1433750947875&channel=GooglePLA&ireid=154294577&fdid=1817&gclid=CjwKCAjw7--KBhAMEiwAxfpkWLjBEYm1Xq9WalA8pvTOkeKmulVKo5y5C-w93s0YvRn4ij1e_SkN7xoC8qQQAvD_BwE
Image 2 Source: https://www.thisiswhyimbroke.com/uk/allure-smart-makeup-mirror/
Image 3 Source: https://www.hackster.io/mprocter12/smart-mirror-using-beaglebone-black-e379a3
Image 4 Source: https://www.hackster.io/eben-kouao/smart-mirror-touchscreen-with-face-recognition-6c84cc

## Slide 3: System Block Diagram
WiFi
Beagle
Bone
Black
USB Client
USB to Computer
LCD Display
USB Hub
P9
P8
USB Host
HDMI
WiFi Adapter
Wall Outlet
Touch
For Development

## Slide 4: Power Block Diagram
5 V
Beagle
Bone
Black
USB Client
USB to Computer
LCD Display
USB Hub
P9
P8
USB Host
HDMI
WiFi Adapter
Wall Outlet
5 V
120 V
60 Hz
5 V
5 V
5 V

## Slide 5: Components / Budget (I/II)
Component | Need to Buy | Cost
One-Way Mirror film | https://www.amazon.com/Daytime-Privacy-Non-Adhesive-Decorative-Control/dp/B07P9Q4ZP8/ref=sxin_14_ac_d_mf_br?ac_md=2-1-V1BDVEVW-ac_d_mf_br_br&cv_ct_cx=mirror%2Bfilm&dchild=1&keywords=mirror%2Bfilm&pd_rd_i=B07P9Q4ZP8&pd_rd_r=1d7b05f1-2ad4-4cfa-9307-6f72e0a1a4f0&pd_rd_w=tlXqf&pd_rd_wg=bZenC&pf_rd_p=b0c493d8-5fdd-4188-b852-c552a4a3abdb&pf_rd_r=88DXCJXG7DY87SM0PR38&qid=1634229290&sr=1-1-ed8a42d3-65f1-4884-a3a2-0dd6e83b6876&th=1 | $11.99
ELECROW 5 Inch Touchscreen 800x480 TFT LCD Display | https://www.amazon.com/Elecrow-800x480-Interface-Supports-Raspberry/dp/B013JECYF2/ref=sr_1_1_sspa?dchild=1&keywords=Elecrow+3.5%27%27&qid=1634230384&s=electronics&sr=1-1-spons&psc=1&spLa=ZW5jcnlwdGVkUXVhbGlmaWVyPUEzQks5U01JWTNDMFZDJmVuY3J5cHRlZElkPUEwOTg2MzUwM0hITjNTNFpUS1VCWSZlbmNyeXB0ZWRBZElkPUExMDMxMjUwTTFaMTk3U1lUOENTJndpZGdldE5hbWU9c3BfYXRmJmFjdGlvbj1jbGlja1JlZGlyZWN0JmRvTm90TG9nQ2xpY2s9dHJ1ZQ== | $46.99
WS2812B RGB 5050SMD Individual Addressable 3.3FT 144(2X72) Pixels/m Flexible White PCB Full Color LED Pixel Strip | https://www.amazon.com/BTF-LIGHTING-WS2812B-Individual-Addressable-Waterproof/dp/B01CDTEHRC/ref=sr_1_1_sspa?dchild=1&keywords=ws2812%2Bled%2Bstrip%2Bblackboard&qid=1634231790&sr=8-1-spons&spLa=ZW5jcnlwdGVkUXVhbGlmaWVyPUEzT0NMSzU1RzY2T1k3JmVuY3J5cHRlZElkPUEwNDkxMzQyMTJQQTJLSEtQWThPNSZlbmNyeXB0ZWRBZElkPUEwNDYyMzI3MkgyNE5SRkRaM0FLRyZ3aWRnZXROYW1lPXNwX2F0ZiZhY3Rpb249Y2xpY2tSZWRpcmVjdCZkb05vdExvZ0NsaWNrPXRydWU&th=1 | $22.88
Need all components to be purchased by instructor listed; additional components may be purchased by student

## Slide 6: Components / Budget (II/II)
Component | Need to Buy | Cost
Micro USB to Wall Charger Power Adapter (5V 2A) | https://www.amazon.com/Travel-Charger-Adapter-Samsung-Galaxy/dp/B0117O020U/ref=asc_df_B0117O020U/?tag=hyprod-20&linkCode=df0&hvadid=309812019776&hvpos=&hvnetw=g&hvrand=1582723768149803960&hvpone=&hvptwo=&hvqmt=&hvdev=c&hvdvcmdl=&hvlocint=&hvlocphy=9061124&hvtargid=pla-599718956044&psc=1 | $7.88
BeagleBoard.org BeagleBone Black | N/A | N/A
Buttons | N/A | N/A
Mini USB to USB cable | N/A | N/A
HDMI Male to Male | N/A | N/A
Micro HDMI to HDMI Adapter | N/A | N/A
4-Port USB 2.0 Hub | N/A | N/A
Note: Components with N/A under “Need to Buy” and “Cost” are available in the OEDK

## Slide 7: Summary of Modifications Made to Original Proposal (10/14)
Hardware
Switched from using PocketBeagle to Beagle Bone Black to supply adequate 5V power connection to LCD display screen
Switched from LED strip to individually addressable LEDs (WS2812) so there can also be data connection as opposed to just power connection for LEDs
Added power switch to turn on/off LEDs
Added button to toggle settings because touchscreen capability might not be feasible given that a mirror film will be placed over the screen
Removed V_IN AC connection as there is no need for MicroUSB to Host Computer connection. Revised to only have V_IN USB pin connected to the Wall Adapter
Software
Maintained use of MagicMirror software for development of app modules and easy integration of data

## Slide 8: Summary of Modifications Made to Revised Proposal (11/09)
Hardware
Maintained use of Beagle Bone Black to supply adequate 5V power connection to LCD display screen
Did not incorporate LED strips
Did not incorporate power switch to turn on/off LEDs as computer will run continuously and can be used to power or turn off device instead of device running on solely on wall power
Did not incorporate button to toggle settings because touchscreen capability was feasible
Mirror film did not arrive, instead we received acrylic mirror tile that was difficult to incorporate
Software
Used OpenWeatherMap API to retrieve weather and used story wrapper to retrieve news data
Used pyqt5 to create GUI instead of MagicMirror app